## Slide 1: University of Dayton Wind Tunnel
Director: Dr. Sidaard Gunasekaran, Associate Professor, Mechanical and Aerospace Department
gunasekarans1@udayton.edu
Contraction
Fan
Plenum

## Slide 2: Specifications
Eiffel Type w/16:1 Contraction Ratio
30” X 30” X 90” closed jet Test Section (~0.75 X 0.75 X 2.3 m)/Open jet
6 Anti-Turbulence Screens
60 HP (45 KW) Fan by Hartzell
Measured Turbulence Intensity < 0.1% (by Hot-Wire) in open jet
Speeds from 6.7 m/s (20 ft/s) to 36.7 m/s (120 ft/s)
Reynolds number range: 100,000 to 500,000 (Bluff and streamlined bodies)
4 Interchangeable closed jet Test Sections
Shuttering System (Gust generator)
Test Section Inlet
Direction of Freestream
Collector
Contraction
Plenum
Diffuser
Fan
Collector
Open Jet Test Section
Shuttering System
Shutter Open
Shutter Closed

## Slide 3: Capabilities
Smoke flow visualization in streamwise and cross-stream directions.
Surface flow visualizations using oil/clay/etc.
Particle Image Velocimetry (PIV) in streamwise and cross-stream directions.
Force based testing to obtain aerodynamic coefficients as a function of angle of attack.
Hot-wire anemometry .
On-body and off-body unsteady pressure measurements.
Streamwise gust profile generation with sinusoidal/custom acceleration profiles with max frequency of upto 5 Hz.
Wingtip vortex
Spitfire aircraft model

## Slide 4: Quantitative and Qualitative Measurements
Sensors:
ATI Mini-40
Digital ATI Gamma
Analog ATI Gamma
ATI Nano 25
Aerolab Sting Mount
Single channel Dantec Hot-wire anemometer
Several unsteady pressure transducers (Kulites)
Flow Visualization:
Tuft flow viz
Smoke flow viz
TiO2 surface flow viz
Fluorescent dye flow viz

## Slide 5: Propeller Testing Capabilities

## Slide 6: Particle Image Velocimetry (PIV) Capability
Seeding: Vicount smoke seeder with glycerin-based oil (mean diameter of 0.2 microns).
Light Source: Nd: YAG frequency doubled laser (Quantel Twins CFR 300)
Camera: The Imperx 4 MP B2021 camera with lens control.
Timing Box: Quantum Composer
Data Post Processing: DPIV Software

## Slide 7: Example PIV Results
FOV 1
FOV 2
FOV 3
FOV – Field of View
Eric Insana, “Low Reynolds number experimental aerodynamic verification of the scaled and LEWICE simulated ice accretions in SLD conditions”, Master’s Thesis, 2020, University of Dayton